## Slide 1
ATN IMPLEMENTATION PROGRESS VIEWS OF ATN SYSTEMS, INC.
Paul Hennig, United Airlines
1-847-700-4312 paulhennig@aol.com
Notes: Paul Hennig v: 1 847 700 4312
United Airlines - WHQKA f: 1 847 700 2053
1200 Algonquin Road e: Paulhennig@aol.com
Elk Grove, IL 60007 USA e: Paul.Hennig@ual.com
Staff Engineer - Information Services Division - United Airlines
Rapporteur for United FANS Board and FANS Management Team
Subject Matter Expert - Aeronautical Telecommunication Network
United Alternate on the ATN Systems, Inc. Board of Directors
Advisor to the IATA Delegates on the ICAO ADS and ATN Panels
Chairman and Rapporteur of ICAO ATN Panel, Working Group-1
Advisor to IATA Delegate on ICAO NAT System Planning Group
IATA Member of the ICAO ATNP Configuration Control Board
UAL Member on IATA FOC, Communications Infrastructure WG
Chairman AEEC Datalink Systems SC, Network Management WG

## Slide 2
Presentation Outline
U.S. Airline Business Drivers
  AOC: ACARS Saturation (Now => 2005)
  ATC: Major Hub Gridlock (Now => 2005)
One Program - Tightly Coupled
  ATNSI: Final RRI Software 1Q00
  ARINC: ATN & VM2 Operational 1Q00
  American: PETAL II
  United: Forward Fit Program July 2000
  FAA: CPDLC Builds I - IA - II 4Q01
Notes: Current VHF ACARS capacity cannot handle peak loads, and will reach total saturation in 2005 after all known measures have been taken.
United Airlines’ European operations are hampered today because VHF ACARS is congested; United flights must switch to more costly satellite data link service while in European airspace; A similar situation is imminent at selected U.S. major hub locations.
AAL and AMR SABRE Group’s 1997 study projected ATC gridlock (the inability to maintain scheduled operations) at major U.S. hubs by 2005.
American PETAL II operational date under consideration at PIT/2 meeting Maastricht UAC on 17 & 18 September (was targeted for 4Q99).
On/about July 2000 Priority Forward Fit Program for 46 Airbus and 20 Boeing aircraft approved at the UAL 24 August FANS Board meeting. (Was 52 Airbus, but six firm orders moved to earlier dates; Start date flexible and OPTIONS not considered).
ONE PROGRAM - TIGHTLY COUPLED means multiple entities have individual corporate/government projects in place, but they all interleave with one another forming a single homogeneous data link implementation program.

## Slide 3
ATNSI Corporate Background
Founded in June 1995
Privately Owned by Eleven U.S. Airlines
Public/Private Venture with the U.S. Federal Aviation Administration to:
  Develop critical Aeronautical Telecommunication Network (ATN) products
  Build and install first production article ATN avionics and ground system components
Notes: ATNSI Principal Contact Information:
Fred Abbott/CO, ATNSI BOD, fabbot@coair.com 1 281 985 1259
Rick Barr/FM, ATNSI BOD, rcbarr@fedex.com 1 901 224 5350
Dave Boaz/HA, ATNSI BOD, boaz@hawaiianair.com 1 808 838 5530
Richard Brandenburg Treasurer rbrandenburg@air-transport.org 202 626 4093
Russ Chew/AA, ATNSI BOD, russ_chew@amrcorp.com 1 817 967 5153
Bill Cotton/UA, Chairman ATNSI BOD, bill.cotton@ual.com 1 847 700 4166
James Davey/AL, ATNSI BOD, jim.davey@alaskaair.com 1 206 431 7005
Stephen Genco/TZ, ATNSI BOD, steveg@iquest.net 1 317 243 4522
Scott Hansen, Secretary ATNSI, sehansen@fedex.com 901 395 5029
John Kern/NW, ATNSI BOD, djzisle@soc.nwa.com 1 612 727 6271
Dale Mierisch/US, ATNSI BOD, djm@usairways.com 1 336 744 4720
Mike Murphy, President ATNSI, mike.murphy@atnsi.com 1 703 412 2900
Lee Wallace/5X, ATNSI BOD, flt1Law@air.ups.com 1 502 329 6546
Bill Watts/DL, ATNSI BOD, bill.watts@delta-air.com 1 404 715 7136
Three classes of ATNSI membership (contact President Mike Murphy):
Stockholder, Participant and Observer

## Slide 4
ATNSI Contract Relationships
ACI: Router Reference Implementation (RRI)
  Aeronautical Communication International (ACI) is:
    AIRSYS-ATM
    AlliedSignal
    Honeywell
    Sextant Avionique
    Sofreavia
ARINC: Conformance Test Suite (CTS)
Notes: AIRSYS-ATM formerly known as Thomson-CSF.
VERTEL (OSI software vendor) is an ACI subcontractor.
KEY ACI/RRR & CTS CONTACTS:
Clayton Wood, AlliedSignal 425-885-8128 Clayton.Wood@alliedsignal.com
Scott Madaras, Honeywell 602-436-3783 scott.madaras@cas.honeywell.com
Alexis Grenon, Sextant 33 01 39 45 65 26 alexis.a.g.grenon@cdv.vly.sextant.thomson.fr
Forrest Colliver, Sofreavia 33 5 62 24 56 03 colliverf@tlse.sofreavia.fr
Bruce Morgenstern, ARINC 410-266-4735 bmorgens@arinc.com

## Slide 5
ATNSI RRI Product Infrastructure Support
Air/Ground Subnetworks
VHF
Satellite
HF
Public/Private
Ground Networks
FAA/
CAAs
Aircraft
ATN
= ATNSI
Products
ATN
ATN
ATN
ATN
ATN
ATN
Airlines/
Other
Users
Notes: The ATNSI Router Reference Implementation (RRI) is both the ATN Router, and ATN End System (ES) Communication Code (transport and upper layers).
The ATN Router is critical to the implementation of the ATN internet for the aviation industry. It solves the complex issues of mobile routing, providing aircraft reachability information to Civil Aviation Authorities.
Once the ATNSI RRI product is certified on, and operational approval is obtained for a revenue in-service aircraft, certification credit can be extended to the many aircraft and/or ground systems that operationally use and/or port that product.

## Slide 6
Related RRI Service Interfaces
Subnetwork Access Subsystem
Ground SNDCF/Mobile SNDCF/ISO 8208 (X.25)
Internetworking/Routing Subsystem
CLNP/ES-IS/IDRP
Transport Subsystem
COTP
Upper Layers Subsystem
ACSE/Fast Byte COPP and COSP
Application Service Element (ASE) Subsystem
CM/CPDLC/ADS-A/FIS
A
S
E
R
R
I
Communication
Service
Dialog
Service
Transport
Service
(work in
progress)
Subnetwork
Service
ATN-1
Service
Notes: ATNSI contract with ACI specifies RRI exposed external interfaces at the Dialog Service & Connection Oriented Transport Service Access Points, and at the Subnetwork Dependent Convergence Function Service Access Point. Application Service Element (ASE) software is not under ATNSI contract, nor is Network Management Agent software (not pictured).
The ARINC ATN-1 architecture assumes a Connectionless Transport Service interface to the RRI Connectionless Network Protocol (either exposing the CLNP interface, or adding a CLTP module with exposed external interface).

## Slide 7
ATNSI/ACI Program Participants
ATNSI/ACI
Programs
Avionics Systems
Ground Systems
Service Provider Systems
Conformance Test Systems
Aerospatiale: Early Access Program *
AlliedSignal: ACI Member
Honeywell: ACI Member
Kongsberg: Early Access Program *
Rockwell: Early Access Program *
Sextant: ACI Member
ARINC: Direct Coordination with
ACI or Early Access Program *
EuroVDL: ATNSI Offer of RRI
Software *
FAA: Cooperative Agreement and
ACI Offer of Software *
EUROCONTROL PETAL II:
ATNSI/ACI Offer of Software *
FAA: Cooperative Agreement
EUROCONTROL/ATNSI: Common
American European Reference
ATN Facility (CAERAF)
* - In Coordination
PETAL II/FAA Program Participant
Notes: Kongsberg has M-ADS for Norwegian helicopters in North Sea operations.

## Slide 8
RRI Program Schedule
30 Sep
3Q00
1997
1998
1Q99
2Q99
3Q99
4Q99
1Q00
2Q00
J F M
A M J
J A S
O N D
J F M
A M J
J A S
Project Start
Functional Spec
System Spec
Software Spec
Interface Control Spec
Software Design Spec
Build 1 Software
Build 2 Software
22 Jul
14 Nov
27 Mar
30 Oct
15 Oct
6 Dec
7 Feb
16 May
Pre-Test Software
Software Acceptance
Supporting Documentation
25 Nov
19 Jun
31 May
First Article Inspection
Notes: Software lines-of-code extrapolated from Software Requirements Specification. Dates assume existing resources, and are predicated on software lines-of-code numbers using the SLIM tool. Dates also assume a DO178B “pure” waterfall approach (longest duration subsystem completion prior to commencement of next phase).
Availability of the ARINC VDL Mode 2 ATN-1 Service Interface and Program Development are in coordination, and will not affect above dates.
Product Quality WILL NOT TO BE COMPROMISED! No juggling to meet dates.
All ICAO Possible Defect Reports (PDRs) have been subsumed (ICAO CCB Edition 2.3) ICAO DOC 9705.

## Slide 9
CTS Program Schedule
Planning Documents
23 Dec
4Q99
1997
1Q98
2Q98
3Q98
4Q98
1Q99
2Q99
3Q99
J F M
A M J
J A S
O N D
J F M
A M J
J A S
O N D
Project Start
RRI Test Profiles
Specification
Design
Test Documents
Software Acceptance
1 Jul
21 Apr
23 Jun
10 Dec
1 Nov
1 Nov
Supporting Documentation
Configuration Audit
19 Apr
1 Jun

## Slide 10
Change Management Process
Vendor Internal Programs
  RRI and CTS Teams Each have Internal Change Management Processes for Developmental Activities
ATNSI Project
  ATNSI has a Change Management Process for Functional Project Baseline and all Project Documents (with Traceability to Functional Baseline)
Industry Coordination
  ICAO ATNP Configuration Control Board is Incorporated into ATNSI Change Management Process
Notes: Both Amendment 73 to Annex 10 of the Chicago Convention, and ICAO DOC 9705 (detailed technical ATN Standards and Recommended Practices ) are in effect and published. The ICAO Air Navigation Commission (ANC) established the ATN Panel, Configuration Control Board (CCB) following SARPs Edition 1.0 PHUKET (three months after ATNP/2 met in November 1996). The CCB Edition 2.3 baseline contained in DOC 9705 reflects the culmination of work on a total of 141 Possible Defect Reports (PDRs) submitted since CCB inception. 130 have been completely processed (either WITHDRAWN, REJECTED, FORWARDED or RESOLVED), and 11 were under review as of July 1998. ATNP/3 is set for February 2000.
ICAO and AEEC, together with IATA, are evaluating a process whereby the membership and technical expertise within each organization can be fully assimilated by the other in the area of ATN standardization and validation.

## Slide 11
Tightly Coupled Program
AOC
  ARINC ATN-1 and VM2
  ATNSI AIRLINES
    AAL
    UAL
    OTHERS
ATC
  ATNSI OPS EVAL
  PETAL II
  ProATN
  FAA CPDLC Builds I-IA-II
Notes: AOC
The current ARINC VM2 proposal revolves around a cost reduction for all VM2 equipped aircraft. ARINC will ensure that VM2 service pricing is always more favorable than for comparable ACARS services. ARINC will not charge for any overhead associated with the VM2 protocol.
As part of this proposal, ARINC will continue to support ACARS equipped aircraft as long as spectrum and capacity issues allow, however, as the costs to maintain the outdated ACARS service continue to raise, and as ARINC customers migrate to the new VM2 service, customers remaining on ACARS should expect service price increases. Over time, increasing volumes on VM2 will have a downward impact on VM2 prices, and an upward impact on outdated ACARS prices. Further, after 1 January 2000, any aircraft new to the outdated ACARS service will be charged a premium.
The initial deployment of ground stations will ensure complete en-route coverage over the continental United States by 1 January 2000. Plans are for National and worldwide deployment of ATN compliant ground stations for future CNS/ATM accommodation.
Other network service providers (SITA, AVICOM, etc.) may have similar infrastructure upgrade programs.

## Slide 12
ATNSI Operational Evaluation
Communication Application Services
  Air Traffic Control (ATC)
    Context Management (CM)
    Controller/Pilot Data Link Communications (CPDLC)
  Aeronautical Operational Control (AOC)
Networks
  Aeronautical Telecommunication Network (ATN)
Subnetworks
  VHF Data Link (VDL) Mode 2 (VM2)
  Satellite SATCOM Data-3 (SD3)
  X.25 Ground-Ground
Notes: CERTIFICATION Areas of Responsibility
End-through-End American Airlines / Rockwell Collins
Avionics Human Factors American Airlines
Avionics Subsystems American Airlines / Rockwell Collins
Communications Systems ATNSI / ARINC / ACI
FAA Ground Systems FAA En-Route IPT / Data Link IPT
FAA Human Factors FAA En-Route IPT
Procedures FAA Air Traffic

## Slide 13
Operational Environments
ATC
  PETAL Operational Sectors
    Maastricht (TBD)
    Others TBD
  U.S. En-Route Sectors
    First Site: Miami 4Q01
    All U.S. Domestic Centers 2Q02-2Q03
AOC
  Airline Ground Host Systems 1Q00
Notes: The primary operational focus and schedule driver for this ATN program is PETAL II (Preliminary Eurocontrol Test of Air/ground dataLink).
The Federal Aviation Administration (FAA) counterpart program is expected to be incorporated into the initial certification effort upon FAA approval to implement a compliant program (FAA Joint Resources Council meeting in October 30, 1998).

## Slide 14
ATC Operational Capabilities
Reduction in Airport Departure Delays (1)
  Eliminate Miles-in-Trail Restrictions
  Reduce In-Sector Time & Miles Flown by 20%
Reduction in Airport Arrival Delays (2)
  Eliminate Sector Holding
  Reduce In-Sector Time & Miles Flown by 20%
(1) Increase in departures up to 10% from capacity baseline
(2) Increase in arrivals up to 40% from capacity baseline
Notes: Operational Capabilities will drive the CPDLC/ATN Certification effort. These capabilities dictate the Safety and Interoperability Requirements, and the Procedures for the participating systems and users.
These Operational Capabilities are based on an FAA report titled “User Benefits of Two-Way Data Link Communications” which present the utility of data communications in congested en-route airspace. ATNSI plans to use these targets to validate the ATNSI Operational Evaluation - obviously, at this time, the targets are subject to change (e.g., the study benefits assumed a specific minimum CPDLC message set), but they reflect the type of “Success Criteria” that ATNSI is trying to obtain for their Operational Evaluation.
It is important to note that these Operational Capabilities reflect improvements in the U.S. domestic BUSIEST sectors. Benefits will not be as prevalent in sectors that are not currently at or near existing capacity restrictions. Figures quoted above reflect an end-state environment (80% critical mass), and do not consider interim, mixed fleet equipage.

## Slide 15
Airline Business Case
AOC
  Costs & Risks of Doing Nothing
  VM2 Incentives & ACARS Penalties
  Enabling Technology
ATC
  A Significant Portion of $337 Million detailed in the FAA’s “User Benefits of Two-way Data Link ATC Communications: Aircraft Delay and Flight Efficiency in Congested En Route Airspace”
Layered Communication Software
  Data Communication System & Service Competition
Notes: The CNS/ATM Focused Team (C/AFT) formed the ATS Data Link Focus Group to help resolve economic uncertainty in the industry from an airline perspective by:
Focusing on economic modeling and analysis,
Categorizing data link services according to operational function, and linking operational benefits to each successive “level of service”, and
Using an approach that is operations, not technology driven.

## Slide 16
Next Steps
Interoperability Team Establishment and/or Coordination with Existing:
  PETAL II Integration Team (PIT)
  ARINC VM2 Interoperability Team
Certification Plan Development
Preparation of a Detailed Operational Evaluation Schedule and Script
Notes: Certification Plan
Operational Environment Definitions *
Operational Safety Assessment *
Including Functional Hazard Assessment
Avionics Developer Segment Safety Assessment *
System Requirements and Procedures Document *
Operational Objectives
Safety, Performance, and Interoperability Objectives
(* Based on Guidance from RTCA SC189/EUROCAE WG53)
ATNSI intends to support the RTCA SC189/EUROCAE WG53 process for the certification of data communications systems.

## Slide 17
QUESTIONS?