## Slide 1: Security Infrastructure for ATN
WG1/SG2
Presented by: Simon Blake-Wilson
Allied Signal for NASA Ames

## Slide 2: Outline
Overview:
Information security.
Cryptography.
Public key infrastructures.
Application to ATN.
Goals:
High level overview of ATN security
Motivation for design of solution

## Slide 3: Information Security
Information security is concerned with providing:
Confidentiality,
Integrity, and
Availability
of data (during both storage and communication).

## Slide 4: Threats
Privacy
Authentication
Integrity
Monitoring
Spoofing
Modification
Data Corruption
Virus
Viruses

## Slide 5: Paper Security
Traditionally data has been stored on paper where:
Confidentiality = sealed envelope, trusted carrier
Integrity = paper itself plus handwritten signature
Availability = efficient filing and post service
These solutions don’t work for electronic data.

## Slide 6: Cryptography
Cryptography provides security by transforming the
data itself. It is therefore storage medium
independent and well-suited to electronic data.
Cryptographic schemes provide:
data confidentiality
data integrity
data origin authentication
entity authentication
non-repudiation

## Slide 7: Cryptography (2)
Cryptography is widely used today in, for example:
Banking and commerce
Cellular telephony
Internet
Military
Two types of cryptographic scheme are in use:
symmetric schemes and public key schemes.

## Slide 8: Symmetric Cryptography
In a symmetric cryptographic scheme, Alice
and Bob must share a secret key in advance.
Symmetric encryption schemes provide data
confidentiality. Examples: US government’s DES,
AES.
Symmetric message authentication codes or MACs
provide data integrity and data origin authentication.

## Slide 9: Symmetric Encryption Scheme
Hi
Alice
Shared Secret Key
“5gzUpi51KTIXg0G”
ENCRYPT
Ciphertext
“5gzUpi51
KTIXg0G”
Bob
Shared Secret Key
Hi
DECRYPT
Plaintext

## Slide 10: Symmetric MAC
Hi
Alice
Shared Secret Key
MAC
MACed Plaintext
Bob
Shared Secret Key
Tag Check
Hi
Fiepw1jdw
Fiepw1jdw
Hi
Hi
Fiepw1jdw
Fiep

## Slide 11: Pros and Cons of Symmetric Crypto
Pros:
Symmetric cryptography is relatively efficient.
Cons:
How do you achieve non-repudiation?
How do you obtain shared secret keys?

## Slide 12: Symmetric Key Management
Each user shares a key with a trusted key translation
center (KTC).
Alice
Bob
KTC
3. EKBT(k)
1. Request
2. EKAT(k)
A, B
High online workload for KTC. Users trust KTC unconditionally.

## Slide 13: Public-key cryptography
In a public-key cryptographic scheme, each user has
two keys known as a key pair. One key is public, the
other is private.
The mathematical relationship between the keys
ensures knowledge of public key does not
compromise public key.
Public-key encryption schemes provide data
confidentiality. Public key signature schemes
provides data integrity, data origin authentication,
and non-repudiation.

## Slide 14: Public-key Encryption Scheme
Hi
Bob’s Public Key
“5gzUpi51KTIXg0G”
ENCRYPT
Ciphertext
“5gzUpi51
KTIXg0G”
Bob
Hi
DECRYPT
Plaintext
Bob’s Secret Key

## Slide 15: Public-key Signature Scheme
Hi
Alice
Alice’s Private Key
SIGN
Signed Plaintext
Bob
Alice’s Public Key
VERIFY
Hi
Fiepw1jdw
Fiepw1jdw
Hi
Hi
Fiepw1jdw
Fiep

## Slide 16: Bases for Public-key Schemes
Integer factorization problem
  1978
  RSA, 1024 bit keys, widely used
Discrete logarithm problem
  1976
  DSA and Diffie-Hellman, 1024 bit keys
Elliptic curves
  1985
  ECDSA and EC Diffie-Hellman, 160 bit keys

## Slide 17: Pros and Cons of Public-key Crypto
Pros:
Improved key management
Non-repudiation available
Cons:
More computational overhead
More bandwidth

## Slide 18: Hybrid Solution - Key Exchange
Bob’s Public Key
“5gzUpi51KTIXg0G”
PK ENCRYPT
secret key,
SY ENCRYPT data
“5gzUpi51
KTIXg0G”
Bob
Hi
PK DECRYPT
secret key,
SY DECRYPT
ciphertext
Plaintext
Hi
Bob’s Secret Key
Encrypted key plus ciphertext

## Slide 19: Public Key Distribution
Problem: in a public-key scheme, Alice needs a
genuine copy of Bob’s public key.
Otherwise an attacker can substitute a fake key as
Bob’s key and use this to impersonate Bob.
Analogous to an attacker obtaining your blank
credit card and signing it themselves.

## Slide 20: Certificates to the rescue!
Certificate Authority (CA) binds Bob and his public
key.
Bob goes to the CA with his public key.
CA issues a certificate to Bob containing his identity, his public key, and the CA’s signature on his identity and public key.
Alice obtains the CA’s public key.
Alice verifies the CA’s signature on Bob’s certificate and retrieves his public key.

## Slide 21: X.509 Certificates
Extensions
Additional unique identifiers
Subject’s public key information
(Algorithm ID, public key value)
Subject’s X.500 name
Validity period
CA’s X.500 name
CA’s signature algorithm ID
Certificate serial number
Certificate version
CA’s digital signature
Signature
generation
CA’s
signing
key

## Slide 22: Certification Issues
Certification can solve the public key certification
problem. Unlike KTCs, CAs can be off-line and are
not unconditionally trusted.
However CAs do take on significant liability, they
have high security requirements, and they need
supporting infrastructure - Public Key Infrastructure
or PKI. Furthermore, issues need to be addressed:
Multiple CAs.
Revocation.
Certificate size (X.509 cert size often 20K).

## Slide 23: Multiple CAs - Strict Hierarchy
CA
Root CA
CA1
CA2
CA3
A1
A2
A3
A4
A5
A6
Multiple CAs can be arranged in a hierarchy. High level CAs certify lower CAs. Problem: root CA.

## Slide 24: Multiple CAs - Cross-certification
CA1
A1
A2
A3
CA2
A4
A5
A6
CAs issue each other certificates (cross-certification).
Problems: liability and cross-certification management.

## Slide 25: Revocation
Certificates may need to be revoked because:
Suspicion of key compromise.
Subject leaves organization.
Subject changes role in organization.
Example: Scotiabank’s internet banking PKI.
90026 certificates issued. Over 19000 revoked
so far.

## Slide 26: Revocation (2)
Most widely used solution: certificate revocation
lists. Each CA regularly produces a signed list known
as a certificate revocation list or CRL of the serial
numbers of revoked certificates.
Problems: CRL distribution and CRL size.
Alternatives:
Ignore revocation.
On-line certificate status checking

## Slide 27: Morals
Cryptography provides a flexible way to secure electronic data.
A combination of symmetric and public-key cryptography is appealing.
PKI used to distribute public keys.
But:
Security doesn’t come free. Overhead + infrastructure + management.

## Slide 28: Security in ATN
Basis for selecting security solution: ATN
requirement to mitigate the following threats:
Masquerade/modification/replay of air-ground application communications.
Denial of service by flooding ground IDRP databases.
Some additional concerns about air IDRP databases
and ground-ground application communications.

## Slide 29: Security in ATN (2)
WG1/SG2 has therefore provided mechanisms which
may be used for:
Authentication and integrity of air-ground application communications which use ATN upper layers.
Authentication and integrity of air-ground IDRP communications.
Supporting infrastructure.
Also authentication of ground-ground apps, ground-
ground IDRP, AMHS.

## Slide 30: Air-ground Applications
Hybrid symmetric (HMAC) & public-key (ECDSA and EC Diffie-Hellman) solution.
Based on ISO GULS standards.
Mutual authentication during initial contact with a regional CMA.
Initial contact also establishes shared public value and delivers public keys of applications to aircraft.
Application (and location) specific session keys derived by applications from their key pairs and shared public value.
Subsequent application communications secured using MAC under session key
Counter and source included to prevent replay.

## Slide 31: Air-ground Applications (2)

## Slide 32: Air-ground Applications (3)
Typical RF cost: initial CMA contact - say CM-logon:
logon-req: 400 bits
logon-resp: 1500 bits (2/3’s of this is certificate)
Typical RF cost: each subsequent secure message:
32 bits (MAC tag)
Considerable effort to minimize RF cost - recall X.509
certificate often 20K.

## Slide 33: Air-ground IDRP
Hybrid symmetric (HMAC) & public-key (ECDSA and EC Diffie-Hellman) solution.
Session key establishment with either unilateral implicit authentication of aircraft or mutual implicit authentication during IDRP OPEN exchange.
Subsequent communications secured using MAC under session key.
Counter (already present) prevents replay.

## Slide 34: Air-ground IDRP (2)

## Slide 35: Air-ground IDRP (3)
Typical RF cost (unilateral authentication of aircraft):
initial IDRP OPEN:
ground IDRP OPEN: 350 bits
aircraft IDRP OPEN: 32 bits
Subsequent IDRP communications:
no additional bits

## Slide 36: Ground-ground applications
Public-key solution (ECDSA).
Again GULS based.
Commnications secured by signature.
Time field included to prevent replay.

## Slide 37: Ground-ground IDRP
Hybrid symmetric (HMAC) & public-key (ECDSA and EC Diffie-Hellman) solution.
Identical to air-ground IDRP solution.

## Slide 38: AMHS
Public-key solution (ECDSA).
Based on ISO X.400 security standards.
Messages are secured by signature.
Time variant parameter field and recipient identity included to prevent replay and redirection.

## Slide 39: Supporting Infrastructure
ATN entities require secure module to generate and store keys and security related databases, and to perform crypto processing.
ATN PKI to distribute public keys.
Information on security management and security policies as guidance.

## Slide 40: ATN PKI
Major components: CAs and Certificate Delivery Services.
Each State required to have CA and Delivery Services in place and ensure they are maintained.
Aircraft Operating Entities may operate subordinate CAs
CAs issue X.509 certificates and CRLs.
Delivery Services deliver certificates and CRLs to ATN entities.
Sharing CAs recommended.
Delivery Services may be based on directory services. (Or may not!)

## Slide 41: ATN PKI (2)
State CA
State CA
State CA
Ground CMA
AOE CAs
Ground Apps
Ground Routers
Aircraft CMAs
Aircraft Routers

## Slide 42: Certificate Delivery Services
Certificate Delivery Services deliver certificates and CRLs to ATN entities.
X.500 directory likely to help on the ground.
Ground scenarios:
  All applications and routers have directory access.
  CMA has directory access and provides certificates and CRLs as needed to other applications.
  Certificates are pre-stored (initial deployment only?)
Air scenarios:
  Short-lived certificates for CMA/routers sent to aircraft.
  Certificate fields known by aircraft in advance not sent on RF. Certificate reconstructed by aircraft before verification.
  CMA certificates pre-stored (initial deployment only?)

## Slide 43: Summary
WG1/SG2 has developed security solutions to mitigate ATN threats identified by risk analysis.
Solutions use both symmetric and public-key cryptography.
PKI required to support key management.
Considerable effort to minimze cost of solution, and, in particular, use of RF bandwidth.

## Slide 44: Future Issues
Some issues it may be desirable to address post
ATNP3:
Confidentiality
GACS security
Additional guidance on security management and security policies (based on validation experience)

## Slide 45: To find out more...
“Concept” papers:
WG1/SG2 working paper: “Application security solution for the ATN”
WG1/SG2 working paper: “Public key infrastructure for ATN”
Specifications:
Draft SARPS SV8
...or hassle Mike Bigelow.