## Slide 1: SITA Messaging Services & Plans for AMHS
Mansour Rezaei Mazinani

## Slide 2: Agenda
Background
SITA X.400 and AFTN Services
Plans for AMHS
AMHS recommendations and proposal

## Slide 3: Background
ATN-P Subgroup 1 has defined the use of AMHS for ground-ground messaging and transition from AFTN to AMHS
AMHS fully complies with ITU X.400 standards with a global ADMD name “ICAO” under the country code “XX”
Several ATSs already have an operational AMHS service in place, or plan to do so within short term
Because of limited commercial success several public X.400 services are closing down
SITA continues to provide X.400 and AFTN services, and plans for AMHS services to assist and support the transition from AFTN TO AMHS

## Slide 4: SITA Messaging Services
Airline Messaging domain
  Type B Services (MQ-Type-B, MATIP-Type-B ..)
  Web-Type B and SITATEX
X.400 Messaging domain
  X.400 Relay Service (PRMD to PRMD/ADMD)
  X.400 Mailbox; GMS Mail
AFTN Messaging domain
  Direct Connections to AFTN networks for message delivery to airlines
SMTP Messaging domain
  SMTP Relay Service (private & open Internet)
  SMTP Mailbox; PoP3, IMAP4, Web
Delivery to other domains (Gateways)
  Gateways to FAX and TELEX services
  Inter-domain Messaging gateways, Internet Gateway
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: SITA Messaging Services
SMTP
Gateway
Type B MB
Type B
Service
X.400 MB
X.400
ADMD
Telex
Fax
AFTN
Other
VANS
SITATEX Web-TypeB
Internet
GMS Mail
s/w
X.400Mail,
MS Exchange
Type B Domain
X.400 Domain
SMTP Domain
SMTP
MB
SMTP
Relay
Notes: <number>
<footer>
<header>
<date/time>
09/08/97
6
SITA EQUANT VAS Sales Training
Global Messaging Services
04/17/97
13
AOv1mes.ppt
SITA EQUANT Messaging/EC/Notes MSG Overview

## Slide 6: SITA X.400 Services
SITA operates a full X.400 ADMD since 1989 with more than 30 interconnections with other public ADMDs
Secure and reliable for operational message communications over the largest network in the world
Choice of technologies to suit the ATS community current and future plans
Covers three key areas:
  X.400 MTA connections (ADMD-PRMD),
  UA/PC connections: GMS Mail (Mailbox service),
  Gateways to other messaging domains
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: SITA X.400 Services
X.400 ADMD (A=SITAMAIL) & P7 Mailbox Services
Interconnected to third-party ADMDs
AMHS server connectivity using X.25 or IP (RFC1006) based network services
Fully managed single service providing high availability, end-to-end responsibility
‘Country code = WW’ reduces addressing administration

## Slide 8: SITA X.400 Services
Security & reliability
  Positive user identification before connection made
  End to end security across the Global Network
  Central MHS platforms duplicated for reliability
24/7 Global support
Global reach

## Slide 9: SITA X.400 Services

## Slide 10: GMS Mail - P7 Mailbox Service
A global, X.400 standards based service for the low volume business user
P7 based Mailbox service with X.25, TCP/IP or X.28 (Dial-up) connection for small offices/remote locations
Efficient local management of incoming e-mail, address book with aliases, foldering and retrieval, multiple document attachments, rich set of features
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: GMS Mail - Extending the reach
X.28
GMS
Mail
Remote Office
Small Offices
Small Offices
GMS
X.400
X.400 Customers
SMTP
Customers
Airline
Messaging
Internet
Email
ADMD
X
ADMD
Y
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: X.400 Security Overview
X.400 messaging facilities are designed to counter
the following threats:
Masquerade MTS user: Impersonation of one UA or MS by another in order to get unauthorized access to MTS to falsely claim to originate a message or acknowledge receipt
Masquerade MTA: Impersonation of an MTA to a UA or other MTA
Modification of information: Modification or destruction of messages
Information leakage: Loss of confidentiality
Repudiation: Denial of delivery by a recipient or denial of origin by an originator or denial of submission by an MTA

## Slide 13: How Real is the Security Risk
Results for 2001 from the Computer Security Institute’s/ FBI’s annual “Computer Crime and Security” survey show that:
  85% of respondents detected computer security breaches within the last twelve months
  More respondents (70%) cited the Internet as the most frequent origin of attack than those citing internal origin (31%)
  64% acknowledged financial losses due to computer breaches
  91% of respondents detected employee abuse of Internet access privileges
  94% detected computer viruses
Notes: The Computer Security Institute, in partnership with the U.S. FBI, annually document the results of their “Computer Crime and Security” survey. Although these numbers are specific to the U.S., the dangers that they identify are present globally (discuss bullets). Keep these numbers in mind as we get into discussing ISS’ suite of managed security services and how they can help organizations to combat just these types of incidents.

## Slide 14: SITA’S Security Solutions
Consultancy
Managed Security Solutions
  Authentication
  Firewall’s
  Intrusion Protection
  Vulnerability Analysis
  PKI
  VPN’s
Security Solution Design and Installation

## Slide 15: AFTN service overview
SITA
Airline A
Airline B
Airline C
Airline D
Type B connections
AFTN connections
AFTN to AFTN
SITA to/fm AFTN
AFTN2
AFTN1
AFTN4
AFTN3

## Slide 16: AFTN service overview
Two service types are in use:
  Type B - AFTN gateway service
    format control
    address mapping
    priority mapping
  AFTN-AFTN communication service
    limited service through Type B
Currently 70 AFTN connections, mainly for communications with the airlines

## Slide 17: Plans for AMHS
SITA plans to complement the existing services for a complete Messaging service to ATSOs including:
  Fully tested AMHS relay and mailbox services
  AMHS gateways to AFTN and airline messaging
  PRMD hosting services
  Consultancy and partnership for deployment and migration
Provision of different services will depend on community plans for a regional, global or back up use

## Slide 18: Plans for AMHS
The AMHS architecture includes the following components:
    MTA/MS (ATS Message Server)
    DS (X.500/88 Directory Server)
    Communication stacks (ATN, LAN, WAN)
    AFTN/AMHS gateway
    UA (AMHS terminal)
    Integration with the existing SITA Messaging services for communications to AFTN, Type B, SMTP, Internet email, fax and telex.

## Slide 19: AMHS Recommendations
Solution 1: Interconnection of physical PRMDs using A=ICAO virtual ADMD, Transposing the existing AFTN model
  No end to end responsibility
  No global monitoring and problem tracking
  Weak back up in case of one PRMD failure
  Alternate route requires additional interconnections
  Slow migration to AMHS

## Slide 20: AMHS Recommendations
Solution 2: A global physical ICAO ADMD domain to interconnect PRMDs
  ICAO controls domain administration
  Requires to be on dedicated infrastructure
  Needs to have the global reach to facilitate the interconnection
  Clear global responsibility and supervision
  Performent and cost effective
  Facilitates migration

## Slide 21: AMHS Recommendations
Use of a global ADMD for back up and for alternate routing
  Needs to be globally defined for full delivery to all related PRMDs
  If national ADMDs are used, C=XX/A=ICAO needs to be agreed by all ADMDs within the path which results in lengthy interconnections, poor performance and supervision

## Slide 22: AMHS Recommendations
The global communications and its efficient management can be achieved by:
  A physical ICAO ADMD with dedicated and fully redundant infrastructure with local connections and global reach
  Gateways to AFTN and airline messaging for seamless communications and migration
  Round the clock support and end to end supervision necessary for mission critical messaging
  Appropriate services and support for countries where a full service does not justify or assistance required (e.g. fully managed PRMD)

## Slide 23
Regional
IP backbone
Regional
IP backbone
Regional
IP backbone
AMHS ADMD
AFTN GW
AMHS ADMD
AFTN GW
AMHS ADMD
AFTN GW
AM1 AFTN
server
AP1 AFTN
server
AP2 AMHS
PRMD
AP1 AMHS
PRMD
EU1 AMHS
PRMD
EU2 AMHS
PRMD
AM1 AMHS
PRMD
AM2 AMHS
PRMD
X.25
X.25
AMHS Recommendations

## Slide 24: Proposal
SITA is the Air Transport Industry leading for PREMIUM QUALITY Messaging service switching some 25 M messages per day
More than 600 airlines and related business partners trust SITA for delivery of MISSION and TIME CRITICAL Messages
SITA proposes to be the partner of choice for ATSOs for global ADMD, managed PRMD, back up and gateway services according to community or ATSO requirements
A community agreement and feed back is important to direct the required services for effective deployment of AMHS

## Slide 25
Thank you for your attention