## Slide 1: Potential Use of TCP/IP in Aviation
Presented to
United Airlines
April 9, 2001
Computer Networks & Software, Inc.
7405 Alban Station Court, Suite B201, Springfield, Virginia 22150-2318 (703) 644-2103

## Slide 2
Agenda
Introduction
Technical Description ATN and TCP/IP
Future Benefit Analysis
Comparable Cost Analysis
Architecture/Protocol Comparisons
Summary and Recommendations
All information contained in this document is presented for research discussion purposes only and is not endorsed nor approved by any NASA components or individuals.

## Slide 3: Today’s Objectives
Foster awareness of the NASA IP-based activities.
Assess industry future benefits from using IP-based protocols.
Seek guidance for future NASA research activities.
Assess the need to form an industry forum to focus initiatives.

## Slide 4: Corporate Profiles
CNS and MAI have worked together as a virtual company for the last 4 years.
CNS
  Provided comprehensive information technology services for over 12 years
MAI
  Provided technical services to industry and government agencies for over 17 years.
CNS/MAI together provide information technology solutions and products.
Located in Springfield, VA

## Slide 5: NASA John H. Glenn Research Center
Aviation Capacity/Adv Air Transportation Technologies:
Advanced Communications for Air Traffic Management (AC/ATM)
  Satellite Communications
  CNS for Distributed Air-Ground Traffic Management
Aviation Safety/Weather Accident Prevention:
  Weather Information Communications (WINCOMM)
  Air Transport to General Aviation
  National and Worldwide Datalink Communications
Small Aircraft Transportation System:
Airborne Internet
Chart Source: NASA GRC Presentation to the AEEC Data Link Users Forum, 2/07/01

## Slide 6: Challenge for the Aeronautical World
Can the TCP/IP protocol meet aeronautical requirements?
Benefits:
  Lower Infrastructure Cost
  Potential for New Services, such as:
    VoIP
    Multicast
    Security
    Integration with Public Infrastructure
Challenges:
Modifying Political Agreements/Industry Standards
Addressing Technical Issues for:
  Mobility Management
  Policy Based Routing Capability

## Slide 7: Today’s Briefing is the Results of a Series of Studies
Aeronautical Applications over TCP/IP and ATN
Potential Aviation Enhancements Achievable
Through the Use of TCP/IP
ATN Transport and Network Layers Implementation Cost Analysis
TCP/IP Architecture for Aviation
Studies performed under funding from the NASA Glenn Research Center

## Slide 8
Elements of the Study
Technical comparisons of ATN and TCP/IP
Identification of IP based services beyond the current ICAO ATN
  File Transfer
  Voice over IP
  Web-Casting
  Multicasting
  Streaming Media
  Quality of Service
  Security
  Network Management

## Slide 9
Elements of the Study (Cont’d)
Wireless industry developments
Related industry programs and standards
Operational analysis of future use of IP based services
  Context: Requirements as projected in Free Flight DAG-TM
  Analysis of a number of aviation processes and events
  Identification of the use for IP based services in future aviation processes

## Slide 10: Application Categories (Voice and Data)
Air Traffic Management (ATM)
  Air Traffic Control (ATC)
  Air Traffic Services (ATS)
  Communication, Navigation, & Surveillance (CNS)
Airline Operational Communications (AOC)
  Flight Operations
  Maintenance
  Airport/Ramp Operations
Airline Administrative Communications (AAC)
Airline Passenger Communications (APC)
Entertainment

## Slide 11: Evolution of Aviation Wireless Communications
1960
1965
1970
1975
1980
1985
1990
1995
2000
2005
2010
2015
2020
PanAm Satcom Demo
FANS Committee
VDL Mode 2
CPDLC I&IA
PETAL II & LINK 2000
ATN - ISO Definition
GPS
SATCOM (ATS, AOC, APC)
ADLS II & III
NEXCOM VDL Mode 3
VDL Mode 4
CNS/ATM - FANS 1&A
2025+
ACARS
EACARS & AVPAC Attempts
Passenger Telephone Systems
HF Data Link
ATN - IPv? Definition
SATS

## Slide 12
Technical Description ATN and TCP/IP

## Slide 13: Aeronautical Telecommunication (ATN) Network Environment
ATN ROUTER
ATN ROUTER
ATN ROUTER
Avionics Subnetwork
Mode S Subnetwork
HF Subnetwork
Satellite Subnetwork
VHF Subnetwork
CAA Ground Subnetwork
Management
Processor
ATN End System
Aeronautical
Operations
Data Base
ATN End System
Data Display
Processor
ATN End System
Data Entry
Processor
ATN End System
Management
Processor
ATN End System
Aeronautical
Operations
Control
ATN End System
Weather
Data Base
ATN End System
ATC
ATN End System
FIS
Data Base
ATN End System
Weather
Data Base
ATN End System
Service Provider
Ground Subnetwork
Airline Ground
Subnetwork

## Slide 14: Today’s ATN Status
Standards started late 1980’s
ICAO - 91 Nations Agreement 1991
Several Cooperative Attempts - Stalled out but lead to FANS 1/A
FAA Funded Router Development - ATNS, Inc.
European, Eurocontrol early trials
Published Standards - SARPs Edition 3, in 2001
Limited ATN Router Availability
Wireless Components now available
FAA CPDLC I - Operational end of 2002
FAA CPDLC IA - IOC 2003

## Slide 15: Aeronautical Communication Requirements
Interoperability with existing networks
High availability
Mobile communication
Message prioritization
Policy based routing
Security

## Slide 16: ATN Architecture
Consists of applications and communication services that allow
ground, air-ground, and avionics sub-networks to inter-operate
End System(ES)
Application
Entity
Upper Layer
Communications
Service
Internet
Communications
Service
Intermediate
System (IS)
Application
Entity
Upper Layer
Communications
Service
Internet
Communications
Service
Intermediate
System (IS)
Subnetwork
Subnetwork
Subnetwork
End System(ES)
  Context Management (CM) Application
  Automatic Dependent Surveillance (ADS)
  Controller Pilot Data Link Communication (CPDLC)
  Flight Information Service (FIS)
  ATS Message Handling Services (ATSMHS)

## Slide 17: ATN Protocol Architecture
Application
Connection Oriented
Session Protocol (COSP)
Transport Layer (TP4)
Network Layer (CLNP)
Air-Ground
Subnetwork
Ground-Ground
Subnetwork
Application Service Element
(ASE)
Dialog Service (DS)
Control
Function
(CF)
Application
Layer
Application
Transport Layer (TP4)
Network Layer (CLNP)
Air-Ground
Subnetwork
Ground-Ground
Subnetwork
ASE
DS
ACSE
CF
Fast Byte COPP
and COSP
Connection Oriented
Presentation Protocol (COPP)
Sub
Networks
Association Control Service
Element (ACSE)
ISO
Air-Ground
Fast Byte approach selected to obtain bit efficiency over the Air-Ground Link

## Slide 18: ATN and TCP/IP Protocol Architecture
Transport Layer (TCP)
Network Layer (IP)
Air-Ground
Subnetwork
Ground-Ground
Subnetwork
Transport Layer (TP4)
Network Layer (CLNP)
Air-Ground
Subnetwork
Ground-Ground
Subnetwork
Application
ASE
DS
ACSE
CF
Fast Byte COPP
and COSP
Application
ATN Architecture
TCP/IP Architecture
With the Fast Byte enhancements, the two architectures appear similar in structure

## Slide 19
Features and Capabilities
ATN
TCP/IPv6
Air-Ground Architecture
Functionally equivalent
Functionally equivalent
Ground-Ground Architecture
Full Stack and complex
Same as Air-Ground
Mobility Support
Limited Support
Full support-including
mobility within mobility
Quality of Service (QoS)
Limited Services - priorities
Flows, TOS, DiffServ,
RSVP, Real time protocols
Security
Security Label-Limited
Capability-future based on
PKI
IP Security (IPSec), more
Capabilities, PKI available
now
Multicasting
No support
Full support
Network Management
CMIP based -complex
SNMP based - simple
Cost
Few developer, expensive
Widely used, less expensive
ATN and TCP/IP Architecture Comparison

## Slide 20
Future Services Discussion Example
CN (RFC 1122 Compliant LAN)
CMU
FMC
PN (profiled RFC 1122 LAN)
TCP
IPv4
TCP
IPv4
ATN STACK
CM
ASE
CPDLC
ASE
ADS
ASE
FIS
ASE
CM
User
FIS User
ADS
Gateway
CPDLC
Gateway
Other
Apps
Air-Ground Subnetwork
ADS
User
CPDLC
User
Other
Apps
CABIN
Broadband Satcom
Commercial SAT Provider
ASI
ASI
Future AOC Path
Future ATN/FIS Path
GW
Router
Profiled Network (PN)
Compliant Network (CN)
Work under AEEC ATN WG 637 and ADN WG 664

## Slide 21
Comparable Cost Analysis

## Slide 22: TCP/IPv6 vs TP4/CLNP Costing
Task: Technical analysis shows that TCP/IPv6 can support ATN applications. What is the cost difference?
Study Boundaries
  Addresses only the transport and network layer costs associated with the implementation of ATN applications
  Applies to air/ground and ground/ground communications
  Covers the period of 2001 - 2020
  Limited to US aircraft and ground facilities
Principles
  Emphasis on cost differences
  Minimum cost implementations
  Business case support

## Slide 23: Assumptions
The transport and network layers (aircraft and ground) are independent of the ATN application that uses them.
ATC applications, such as CM and CPDLC, will require a dedicated router aboard the aircraft.
The aircraft ES and IS functionality will reside in the same component; e.g., Collins CMU.
Aircraft flying in controlled enroute airspace (above 18,000 feet) will use ATN by 2020.
FAA will not mandate the use of ATN applications for entry into terminal airspace prior to 2020.
ATN equipped aircraft will employ ATN applications in all phases of flight and the ground infrastructure will be equipped to support them.

## Slide 24: Software Costs Only Rationale
Aircraft ES and IS
  Collins purchased software from Airtel.
  Other CMU development, testing, and production cost would likely be equal.
  Since other CMU functionalities would be the same, CMU price would differ by the cost of the software plus a markup.
A/G and G/G Routers
  A/G and G/G routers are same device equipped with different interface cards.
  Router hardware that would support CLNP is probably similar to that needed for IPv6.
  Implement network protocol through software load.
  Principal cost difference is for software.
Ground ES
  Hardware will be identical or essentially equal for either a TP4/CLNP or TCP/IPv6 implementation.
  ES software loaded similar to OS (e.g., Windows 98).

## Slide 25: TP4/CLNP Software Prices
Airborne ES & IS
  Initial fee distributed over 1,000 products
  25% markup
All others
  25% markup

## Slide 26: TCP/IPv6 Software Prices

## Slide 27: Life Cycle Cost Results
TP4/CLNP is 28 times more expensive to implement than TCP/IPv6.

## Slide 28: Cost by Organization

## Slide 29
Protocol Comparisons

## Slide 30: Approach: Analysis Steps
Task 1
ATN Architecture Model
Task 2
ATN TP4
Specification
Task 3
ATN
Specifications
Task 4
TCP/IP
Arch. Model
Task 5
TCP
Specification
Task 6
IP
Specifications
Comparison
Task 7
Requirement
Not met
Task 8
RFC Style
Specification
Comparison

## Slide 31: TCP and TP4 Features Comparison
Both support Connection-oriented and Connectionless Transport services

## Slide 32: Network Service: CNLP vs IP
Both support Connectionless Network services

## Slide 33: Network Service: CNLP vs IP

## Slide 34: Intra-Domain Routing Protocol
ATN
IS-IS
Link State protocol
Dijkstra’s shortest path first
Level 1 and Level 2 areas
Level 1 partition is repaired
automatically
TCP/IP
OSPF
Link State protocol
Dijkstra’s shortest path first
Two-level hierarchy backbone and attached area
Not repaired at all

## Slide 35: Routing Protocols: ATN vs TCP/IP
ATN
TCP/IP
Intra-Domain
Inter-Domain
ES-Router (LAN)
Router-Router (WAN)
IDRP
BGP-4
OSPF
IS-IS
ES-IS
RIP
OSI routing architecture is almost identical to TCP/IP
ATN
TCP/IP
Interior Gateway Protocol
IS-IS Protocol
Border Gateway Protocol
Interdomain Routing Protocol
Discovery Protocol (ARP)
ES - IS Protocol
Autonomous Systems
Routing Domains

## Slide 36: Inter-Domain Routing Protocol
ATN
Interdomain routing
IDRP
Path - vector
TCP/IP
Interautonomous system routing
BGP-4
Path - Vector

## Slide 37: ES -IS Routing Protocol
An important function is the Discovery Protocol
ES -IS
Media independent
Operated periodically
Uses multicast address
ARP
Extended to include other media
On demand
Uses broadcast address

## Slide 38: QoS - ATN
Class of Communication
  High priority flight safety messages
  Low
Application Priority
Residual Error Rate
Requested QoS
  Transit delay
  Residual Error Rate
  Priority
Priority
  Transport Layer - 0 to 14 levels
  Network layer - 15 to 0 (15 reserved)

## Slide 39: QoS - TCP/IP
Token Bucket Filter
Weighted Fair Queuing
Integrated Service Architecture (IntServ)
  Signaling protocol is RSVP
Random Early Detection (RED)
Differentiated Services (DiffServ)
Issues: Network Policy and Procedures
Manual Configuration
SNMP
LDAP
Common Open Policy Server (COPS)

## Slide 40: Mobility Management - ATN
Mobility support
  Air Initiated
  Ground Initiated
  Air or Ground Initiated
Route Initiation is asymmetrical with the responder configured to listen for Call Indication message on the subnetwork
Handoff based on
  IS-SME (Intermediate System - System Management Entity)
  Joint, Leave & Hand off events
  Based on X.25 subnetwork model

## Slide 41: Mobility Management - TCP/IP
Mobility support
  Mobile IP; support for mobile network as well as mobility within mobility
Can interface to any subnetwork

## Slide 42: Security and Priority
ATN
TCP/IP
Security
Security Label
Options field/ IPSec
Priority
16 priorities
Transport layer
maps to network
layer
Type of Service field
(ToS) in IPv4 and
Class field in IPv6

## Slide 43: Security Services
Key Management
Confidentiality
Non repudiation
Integrity/Authentication
Authorization
Key Issue:
Where (protocol layer) to provide these services.

## Slide 44: ATN Security Services
Goal:
Secure exchange of ATS information
Protection against unauthorized access
ATN Security Services:
Access Control
Authentication
Data Integrity

## Slide 45: ATN Security Services (cont.…)
Message Authentication
  64 bit key between peer entities
  Message Authentication Check (MAC) in each message
Replay Protection
  Unique Message ID or Sequence number for the life time of key
Security Label
  Specified by the transport service user to be associated with TSDU
IDRP
  Type 1, 2 or 3 mechanisms
  Type 1 is based on unencrypted checksum
ATN Security Frame work - PKI

## Slide 46: TCP/IP Security Services
IP Security (IPSec)
  Encapsulating Security Payload (ESP)
  Authentication Header (AH)
Authentication Header (AH) functions
  Proof of data origin, Data Integrity, Anti Replay protection
Encapsulation Security Payload (ESP) functions
  AH functions + data confidentiality
Transport Mode
  Upper layer protocols
Tunnel Mode
  IP Datagrams

## Slide 47: Network Management
SNMP
  Simple
  Optimized to support TCP/IP environment
  Can be extended to support other environment
CMIP (Common Management Information Protocol)
  Design with a goal to provide a common protocol flexible enough to solve all problems
  Complex object oriented model with inheritance and allomorphism
  Need ISO full stack
  ROSE ASE

## Slide 48
Application Categories (Voice and Data)
Air Traffic Management (ATM)
  Air Traffic Control (ATC)
  Air Traffic Services (ATS)
  Communication, Navigation, & Surveillance (CNS)
Airline Operational Communications (AOC)
  Flight Operations
  Maintenance
  Airport/Ramp Operations
Airline Administrative Communications (AAC)
Airline Passenger Communications (APC)
Entertainment
Mobile IPv6
?

## Slide 49
Hybrid ATN/IP Model
ATC Center A
ATC Center B
Ground/Ground
(IP)
Network
AOC Center
- Airline A
AOC/AAC/APC
Air/Ground
(IP)
VHF (ATN-OSI)
GW
GW
= Gateway
Other Airline A Functions
•
Maintenance, etc.
GW
GW

## Slide 50: Network Architecture Framework
Use of IP Internet
Use of COTS products
Multiple Service providers
Minimize Gateways

## Slide 51
Study Conclusions

## Slide 52: Summary and Recommendations
TCP/IPv6 provides equivalent network and transport layer (layers 3 and 4) functionality to meet the requirements of aeronautical applications.
This does not mean TCP/IP based COTS products can be used without modification to meet ATN requirements.
The ATN architecture upper layer standards (layers 5, 6 and 7) provide viable mechanisms for achieving interoperability within the aeronautical community.
Aviation’s use of TCP/IP could yield significant benefits.
An industry initiative is needed to focus work toward building consensus on the use of TCP/IP.

## Slide 53
Technical Conclusions
Air-Ground Architecture: ATN and TCP/IP are functionally equivalent.
Ground-Ground Architecture: ATN uses a more complex, full protocol stack; TCP/IP uses the same protocol stack as the Air-Ground architecture.
Mobility Support: ATN provides limited mobility support, whereas TCP/IP provides full mobility support including mobility within mobility.
Security: ATN presently uses Security Labels, which have limited capability; future security will be based on public key infrastructure (PKI). TCP/IP is IPSec-based, which provides more capability; PKI available now.

## Slide 54
Technical Conclusions (cont’d)
Quality of Service: ATN provides limited service; TCP/IP provides flows, RSVP, DiffServ, and real-time protocols.
Multicasting: ATN does not support; TCP/IP does support.
Network Layer (Packet) Header: ATN requires more processing; TCP/IP uses streamlined header enabling more efficient processing.
Network Management: ATN features CMIS/CMIP, which are more complex and limited in implementation. TCP/IP uses SNMP, which is simple, widely tested and available

## Slide 55
Related Programs Conclusions
Numerous aviation standard building communities are part of the effort defining the future known as free flight.
  However, very few are dealing with the issues of the use of IP-based COTS protocols.
  More awareness must be developed through surveys and by attending these forums to offer new ideas.

## Slide 56: Operational Benefit Conclusions
The review of operational procedures within the context of the DAG (ATM-AOC-FMS) shows that the future IP based services have beneficial use (see Tables).
The airlines are now infusing IP technology into themselves - a trend that will accelerate.
The ATM system, managed in this country by the FAA, lags the business world in many areas. An IP-based strategic vision is lacking.

## Slide 57: Operational Benefit Conclusions (Cont’d)
To maximize the intrinsic safety, flexibility, and capacity enhancements that IP technologies can bring to the Free Flight environment, the ATM system will have to aggressively pursue the necessary upgrades that the airlines will be seeking.
Airlines are already providing some limited communications, but will be driven to provide the services that their most prized customer, the business customer, demands.
Powerful, pervasive partnerships will be based on extensive, personalized service, and demand even more robust, IP-based wireless linkages to the airplane.

## Slide 58: Operational Benefit Conclusions (Cont’d)
The result of this apparently unstoppable domino effect will be fleets of IP-capable aircraft connecting passengers to each other, to the airline, and to the world. Airlines will soon create networked airplanes - connecting passengers, flight attendants, and pilots to each other, as well as to the ground.
Within 10 years, airlines will feature aircraft equipped with wide-band, remote, IP connectivity which could be also used for almost infinite numbers of AOC, AAC, and APC functions.